## Slide 1
DES Encryption Algorithm
FPGA Implementation using Vitis HLS
Target: Xilinx Artix-7 xc7a100tcsg324-1
ADAM Marian-Vladut SAS2
February 2026

## Slide 2
Project Overview
What is DES?
• Data Encryption Standard (FIPS 46-3)
• Symmetric-key block cipher
• 64-bit data blocks
• 56-bit effective key (64-bit with parity)
• 16-round Feistel network structure
Project Goals
• Implement DES encryption in C++
• Synthesize to FPGA hardware using HLS
• Target Artix-7 FPGA (xc7a100t)
• Verify functional correctness
• Analyze hardware resource usage
Technology Stack
Vitis HLS 2025.2
High-Level Synthesis
C++
Implementation
Artix-7 FPGA
Target Device
Verilog/VHDL
RTL Output

## Slide 3
DES Algorithm Structure
Encryption Flow
1. Initial Permutation (IP)
2. Split into L0 and R0 (32-bit each)
3. 16 Feistel Rounds
4. Final Permutation (FP)
5. Output 64-bit ciphertext
Feistel Function f(R, K)
• Expansion (32 to 48 bits)
• XOR with 48-bit subkey
• S-box substitution (48 to 32 bits)
• P-box permutation
Key Components
8 S-Boxes
6-bit input, 4-bit output, Nonlinear substitution
Key Schedule
64-bit key to 16 subkeys, 48-bit each round
Permutations
IP, FP, E, P tables, Bit rearrangement

## Slide 4
HLS Implementation Highlights
Key HLS Pragmas Used
• #pragma HLS UNROLL - Full loop unrolling
• #pragma HLS INLINE - Function merging
• #pragma HLS ARRAY_PARTITION - Parallel array access
• #pragma HLS INTERFACE - I/O port definition
Design Decisions
• All 16 rounds fully unrolled
• S-boxes partitioned for parallel access
• ap_uint<64> for data blocks
• ap_uint<48> for subkeys
• Separate encrypt/decrypt functions
Interface Definition
void des_encrypt(block_t plaintext, block_t key, block_t *ciphertext) { #pragma HLS INTERFACE mode=ap_ctrl_hs port=return #pragma HLS INTERFACE mode=ap_none port=plaintext #pragma HLS INTERFACE mode=ap_none port=key #pragma HLS INTERFACE mode=ap_vld port=ciphertext }
Notes: These pragmas define the physical "pins" or ports on the FPGA chip that allow your DES core to communicate with the rest of the system.
mode=ap_ctrl_hs port=return: This creates the block-level control protocol. It adds hardware signals like ap_start (to begin encryption), ap_ready, and ap_done (to signal completion).
mode=ap_none: This tells the tool that the plaintext and key inputs are simple data wires with no additional handshake logic.
mode=ap_vld port=ciphertext: This adds an "output valid" signal to the ciphertext port. It tells the receiving hardware exactly when the encryption is finished and the data is ready to be read.
#pragma HLS UNROLL:
Used in your permutation and round loops.
Instead of performing 16 rounds sequentially (one after another), "unrolling" creates 16 physical copies of the logic. This allows the FPGA to process the data in parallel rather than waiting for a loop counter to increment
#pragma HLS INLINE eliminates function call overhead by dissolving a sub-function's logic directly into its caller, allowing the hardware compiler to optimize across boundaries and improve bit-level parallelism for tasks like permutations.

## Slide 5
C Simulation Results
ALL TESTS PASSED
9/9
Tests Passed
100%
Pass Rate
0
Errors
Test Vectors Verified
Test Name
Key
Plaintext
Ciphertext
Status
Grabbe Example
133457799BBCDFF1
0123456789ABCDEF
85E813540F0AB405
PASS
Zero Ciphertext
0E329232EA6D0D73
8787878787878787
0000000000000000
PASS
Classic FIPS
FEDCBA9876543210
0123456789ABCDEF
ED39D950FA74BCC4
PASS
Round-Trip
133457799BBCDFF1
DEADBEEFCAFEBABE
Encrypt then Decrypt
PASS
Simulation completed in 1.826 seconds - Vitis HLS 2025.2

## Slide 6
C Synthesis Results
148.72 MHz
Estimated Fmax
10 ns
Target Clock
PASSED
Timing Met
Synthesized Module Hierarchy
des_encrypt (Top-level)
- generate_subkeys
- des_core
- apply_IP (inlined)
- feistel x 16 (unrolled)
- apply_FP (inlined)
Optimizations Applied
• IP_LOOP: 64 iterations - parallel
• FP_LOOP: 64 iterations - parallel
• ROUNDS_LOOP: 16 - fully unrolled
• SBOX_LOOP: 8 - parallel lookup
• All permutation loops unrolled
Synthesis completed in ~40 seconds - RTL generated in Verilog and VHDL

## Slide 7
C/RTL Co-Simulation Results
RTL VERIFICATION PASSED
What is Co-Simulation?
• Verifies synthesized RTL matches C++ behavior
• Runs testbench against actual Verilog/VHDL
• Confirms cycle-accurate functionality
• Validates interface timing
Verification Results
• All test vectors verified in RTL
• Output matches C++ golden model
• No timing violations detected
• Interface handshaking confirmed
Verification Flow Completed
C Simulation
Functional Test
->
C Synthesis
RTL Generation
->
Co-Simulation
RTL Verification

## Slide 8
Summary & Conclusions
[OK]
Functional DES Implementation
Encryption and decryption verified with NIST test vectors
[OK]
Successful HLS Synthesis
148.72 MHz achieved on Artix-7 FPGA (target: 100 MHz)
[OK]
RTL Verification Complete
Co-simulation passed all 9 test cases
[OK]
Fully Parallel Design
All 16 Feistel rounds unrolled in hardware
DES FPGA Implementation - Vitis HLS 2025.2 - Artix-7 xc7a100tcsg324-1